## Slide 1
DHCP snooping is a layer 2 security technology built into the operating system of a capable network switch that drops DHCP traffic determined to be unacceptable. The fundamental use case for DHCP snooping is to prevent unauthorized (rogue) DHCP servers offering IP addresses to DHCP clients. Rogue DHCP servers are often used in man in the middle or denial of service attacks for malicious purposes. However, the most common DoS scenario is that of an end-user plugging in a consumer-grade router at their desk, ignorant that the device they plugged in is a DHCP server by default.
DHCP snooping

## Slide 2
      VLAN Level DHCP Snooping
      Switch Level DHCP Snooping
      DHCP Snooping Traffic Violation Statistics
      DHCP Snooping Option-82 Policy
  Functional Description

## Slide 3: Basic Architecture
The UDP Relay CMM task will maintain three (3) tables to store the DHCP Snooping related configuration data:
The DHCP Snooping VLAN table,
The DHCP Snooping Port table and
The DHCP Snooping Binding table.
The task will look up the configured data in these three tables to filter/screen the DHCP packets appropriately.

## Slide 4
DHCP snooping acts like a firewall between untrusted hosts and DHCP servers. The user can use DHCP snooping to differentiate between untrusted interfaces connected to the end user and trusted interfaces connected to a DHCP server or another switch.
An untrusted message is a message that is received from outside the network or firewall. When DHCP snooping is used in a service-provider environment, an untrusted message is sent from a device that is not in the service-provider network, such as a customer's switch. Messages from unknown devices are untrusted because they could be sources of traffic attacks.

## Slide 5: Ingress Source Filtering
In addition to filtering untrusted DHCP messages, DHCP Snooping can allow user to configure Ingress Source Filtering as a security feature.
When Ingress Source Filtering (ISF) is enabled on a port or linkagg port, the initial packets permitted for traffic are DHCP, DNS and ARP so as to allow the client to obtain and IP address from the DHCP server in which a MAC-IP Binding entry is created in the DHCP Snooping task, it will then allow packets that match the IP address/MAC address/ port combination that is obtained from the DHCP snooping binding table entry.

## Slide 6: DHCP Relay Agent Information Option-82
Option 82 is an option specified by RFC 3046 for DHCP relay agents to insert information in packets forwarded to DCHP servers and to remove that same information before relaying responses back to DHCP clients.
For now, there is no requirement from Access Guardian for DHCP Snooping. User is allowed to configure ISF on AG port just like the other non-AG ports. Detail of DHCP Snooping on an AG port will be described in detail in the later section of this document 8.1.1.R01 release

## Slide 7: Management Interfaces
      Command Line Interface
        Global Commands
          dhcp-snooping admin-state <enable/disable>
        VLAN Table Commands
          dhcp-snooping vlan <vlanId>
        Port Table Commands
        Binding Table Commands
        Ingress Source Filtering Commands
        Show Commands
          show dhcp-snooping
      Web-View
      SNMP

## Slide 8: APPENDIX F: 7.3.4.R01 DHCP Snooping
                Appendix G: PVLAN support for DHCP-Snooping & ISF in 8.3.1.R01
a